## Slide 1: 网络与分布式计算
Networks and Distributed Computing

## Slide 2: 网络与分布式计算
胡继承
武汉大学计算机学院
jicheng @ yahoo . com
https://github.com/network-distributed
计算机学院大楼 E座 E315 房间
办公电话: 027-68776033

## Slide 3: 教材及参考
James F. Kurose and Keith W. Ross, Computer Networking: A Top Down Approach , 7th edition. Pearson Education, 2017.
David Reilly and Michael Reilly, 2004, Java Network Programming and Distributed Computing, 清华大学出版社
本课程的幻灯片改编自教材作者配套幻灯片
Slides of this course are adapted from J.F Kurose and K.W. Ross

## Slide 4: 课程要求
课堂要求
  保持课堂安静
  多动手练习、多写代码
  不缺课
  不迟到
让教学过程成为增长知识、钻研学术的乐之者之旅
阅读
上网搜索并钻研
编码

## Slide 5: 课程成绩评定方式
期末考试 – 70 %
平时 – 30 %
    实验报告 – 作为单独的实验课给成绩, 实验课和理论课务必选同一教师的授课，不然无法给出成绩
    测验 / 代码 – 10 %
    小作品 / 作业 – 10 %
    考勤 – 10 %

## Slide 6: 现在正式开始教学 ...

## Slide 7: 第一章 导论
本章欲达成目标:
找点感觉、熟悉术语
更深入详细的内容在后续课程教学中逐渐展开
方法:
  以互联网作为例子
概述:
什么是互联网?
什么是协议?
网络边缘: 主机, 接入网, 物理媒介
网络核心: 分组/电路交换, 互联网结构
性能: 丢包, 延迟, 吞吐量
安全
协议层次, 服务模型
历史

## Slide 8: 第一章: 提要
  1.1 什么是互联网?
  1.2 网络边缘
    端系统, 接入网, 链路
  1.3 网络核心
    电路交换, 分组交换, 网络结构
  1.4 分组交换网络的时延、丢包和吞吐量
  1.5 协议层次, 服务模型
  1.6 网络攻击: 安全
  1.7 历史

## Slide 9: 什么是互联网: 细节探究
连接的亿万计算装置:
  主机 = 端系统
  运行着 网络 app
传输链路
  光纤, 铜线, 无线电, 卫星
  传输速率: 带宽
分组交换: 转发分组 (数据块)
  路由器 与 交换机
有线连接
无线连接
路由器
智能手机
PC
服务器
无线连接的
笔记本电脑
移动网络
全球 ISP
区域 ISP
家庭网络
机构网络
Notes: 9

## Slide 10: 趣味互联网装设备
IP 相框
http://www.ceiva.com/
网络土司机 +
天气预报
网络电话机
智能冰箱
Slingbox: 远程查
看、控制有线电视
Tweet-a-watt:
用电量监测
智能床垫
小米智能音箱

## Slide 11
互联网: “网络的网络"
  互联的 ISP
协议 控制信息(message)的发送和接收
  e.g., TCP, IP, HTTP, Skype, 802.11
互联网标准
  RFC: Request for comments
  IETF: Internet Engineering Task Force
什么是互联网: 细节探究
移动网络
全球 ISP
区域 ISP
家庭网络
机构网络

## Slide 12: 什么是互联网: 服务的视角
为应用提供服务的基础架构
  Web, VoIP, email, 游戏, 电子商务, 社交网络, AI, …
为app提供编程接口
  一种联网机制使得发送和接收app程序连接到互联网
  提供服务选项，类似于邮政服务
移动网络
全球 ISP
区域 ISP
家庭网络
机构网络

## Slide 13: 什么是协议?
人类交互协议:
“几点了?"
“能问个问题吗？"
介绍
… 特定的信息发出
… 当信息被接收到时特定的动作产生，或者产生其它事件
网络协议:
主体是机器而不是人类
互联网上所有的通讯活动均由协议来控制
协议定义在网络实体之间 发送与接收信息(message)时的格式、顺序, 及信息传输与接收时 采取的动作

## Slide 14
人类交互协议 与 计算机网络协议:
Q: 其它人类交互协议?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.github.com/network-distributed
<file>
time
TCP connection
request
什么是协议?

## Slide 15: 第一章: 目录
  1.1 什么是互联网?
  1.2 网络边缘
    端系统, 接入网, 链路
  1.3 网络核心
    分组交换, 电路交换, 网络结构
  1.4 网络时延, 丢包及吞吐量
  1.5 协议层次, 服务模型
  1.6 网络攻击: 安全
  1.7 历史
Notes: 15

## Slide 16: 近距离观察网络结构:
网络边缘:
  主机: 客户机 与 服务器
  （服务器通常位于数据中心）
接入网物理媒介:
  有线、无线传输链路
网络核心:
  互联的路由器
  网络的网络
移动网络
全球 ISP
区域 ISP
家庭网络
机构网络

## Slide 17: 接入网与物理媒介
Q: 如何连接端系统到边缘路由器?
住宅接入网
机构接入网 (学校, 公司)
移动接入网
熟知:
接入网络的带宽(bits per second) ?
共享还是专用?

## Slide 18: 接入网: DSL (digital subscriber line )
ISP
中心局
电话网络
DSLAM
语音, 数据在专线上
以不同的频率
传输到中心局
  使用已有的电话线连接到中心局的DSLAM
    将DSL电话线上的数据连接到互联网
    将DSL电话线上的语音连接到固话网
  < 2.5 Mbps 上行传输速率(通常 < 1 Mbps)
  < 24 Mbps 下行传输速率(通常 < 10 Mbps)
DSL
调制解调器
分线器
DSL 接入
multiplexer
Notes: multiplexer: MUX, 数字选择器，多路数字选择器

## Slide 19
接入网: 有线网络
有线(猫)
调制解调器
分线器
…
有线头端
频道
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
频分复用: 不同频道通过不同频带进行传输
Notes: multiplexing: 多路复用

## Slide 20
ISP
数据, TV 在共享的
有线分布网络上
以不同的频率传输
有线
调制解调器
分线器
…
有线头端
CMTS
有线调制解调器
终端系统
HFC: hybrid fiber coax（光纤有线混合）
  非对称: 下行传输速率可达到 30Mbps, 上行传输速率 2 Mbps
有线网络, 光纤连接家庭到 ISP 路由器
  家庭 共享接入网络 到有线头端
  与 DSL 专线接入中心局不同
接入网: 有线网络
Notes: Cable modem: 电缆调制解调器，有线调制解调器
CMTS: cable modem termination system

## Slide 21
接入网: 家庭网络
发送/接收 头端 或
中心局
有线或 DSL 调制解调器
路由器, 防火墙, NAT
有线以太网(1 Gbps)
无线AP (接入
Point, 54 Mbps)
无线设备
常整合到单一盒子中

## Slide 22: 企业接入网 (以太网)
通常用于公司，大学校园等
  10 Mbps, 100Mbps, 1Gbps, 10Gbps 传输速率
  今天端系统通常连接到以太网交换机
  工业以太网 – 将以太网应用于工业环境，使用的协议提供仲裁及实时控制
以太网
交换机
机构 mail,
web 服务器
机构路由器
机构连接到
ISP (互联网)

## Slide 23: 无线接入网
共享无线接入网络连接端系统到路由器
  通过基站，亦称接入点(接入 point)
无线局域网:
  大楼内 (100 ft.)
  802.11b/g/n/ac/ax (WiFi): 11M, 54M, 450M, 1G, 4G bps 传输速率
广域无线接入
  由移动运营商提供, 10 公里覆盖
  速率范围 1 到 10 Mbps
  3G, 4G: LTE, 5G(10Gbps)
to 互联网
to 互联网
Notes: 5G网络的主要优势在于，数据传输速率远远高于以前的蜂窝网络，最高可达10Gbit/s，比当前的有线互联网要快，比先前的4G LTE蜂窝网络快100倍。另一个优点是较低的网络延迟（更快的响应时间），低于1毫秒，而4G为30-70毫秒。

## Slide 24: 主机: 发送数据分组
主机发送功能:
获取应用消息(message)
将其分解为小块, 称为分组(packets), 长度 L 比特
以传输速率 R 传输分组到接入网
  链路传输率(link transmission rate), 亦称 链路容量(link capacity), 亦称 链路带宽(link bandwidth)
R: 链路传输率
主机
1
2
两个分组,
每个 L 比特
分组传输时延
传输 L-比特分组
到链路中所需时间
L (比特)
R (比特/秒)
=
=

## Slide 25: 物理媒介
比特: 在收发器之间传
物理链路: 位于收发器之间
导向媒介:
  信号在实体媒介中传播: 铜线, 光纤, 同轴电缆
非导向媒介:
  信号自由传输, 例如无线电
双绞线
互相绝缘的铜线对
  五类: 100 Mbps, 1 Gbps 以太网
  六类: 10Gbps

## Slide 26: 物理媒介: 同轴电缆, 光纤
同轴电缆:
两个同心铜导体
双向
宽频带:
  有线多通道
  HFC
光缆:
玻璃光纤传输光脉冲，每个脉冲1比特
高速运行:
  点对点传输速度高 (例如可到10-100 Gbps 传输速率)
低错误率:
  中继间隔远
  对电磁噪声免疫
Notes: HFC(Hybrid Fiber－Coaxial)：混合光纤同轴电缆

## Slide 27: 物理媒介: 无线电
信号由电磁波谱携带
无物理的”线”
双向
传播环境影响:
  反射
  物体阻挡
  干涉
无线连接类型:
陆地微波
  达到 45 Mbps 通道
局域网 (e.g., WiFi)
  54 Mbps
广域 (e.g., 移动)
  4G 移动: ~ 10 Mbps
卫星
  Kbps to 45Mbps 通道 (或多个小通道)
  270 msec 端到端时延
  地球同步 与 低空

## Slide 28: 第一章: 目录
  1.1 什么是互联网?
  1.2 网络边缘
    端系统, 接入网, 链路
  1.3 网络核心
    分组交换, 电路交换, 网络结构
  1.4 网络时延, 丢包及吞吐量
  1.5 协议层次, 服务模型
  1.6 网络攻击: 安全
  1.7 历史
Notes: 28

## Slide 29: 网络核心
互联的路由器形成织网
分组交换: 主机将应用层的消息(messages)分解为分组
  从源到目标路径所在链路上，依次将分组由一个路由器转发到下一个
  每一分组均按全速链路容量进行传输
Notes: Full link capacity

## Slide 30: 分组交换: 存储转发
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
存储转发: entire packet must arrive at router before it can be transmitted on next link
一跳数字举例:
L = 7.5 Mbits
R = 1.5 Mbps
一跳传输时延 = 5 sec
more on 时延 shortly …
源
R bps
目的
1
2
3
L bits
per packet
R bps
end-end 时延 = 2L/R (assuming zero 传播时延)
Notes: One-hop: 一跳

## Slide 31: 分组交换: queueing 时延, 丢包
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and 丢包:
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 32: Two key 网络-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header

## Slide 33: Alternative core: 电路交换
end-end resources allocated to, reserved for "call" between source & dest:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone 网络s

## Slide 34: 电路交换: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple 接入 control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 35: 分组交换 对比 电路交换
例子:
1 Mb/s 链路
单一用户:
  活跃时100 kb/s
  10% 的时间活跃
电路交换:
  10 个用户
分组交换:
  35 个用户, 大于10个用户同时活跃的概率小于 .0004 *
分组交换接纳更多用户使用网络!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..

## Slide 36
对爆发数据非常好
  资源共享
  简单，无需建立呼叫（no call setup）
可能导致极度拥塞: 分组延迟与丢包
  需要通过协议进行拥塞控制来保证可靠地数据传输
Q: 如何提供类似电路的效果?
  语音/视频应用的带宽保证
  依然未解决(见第7章)
分组交换真的盖了帽吗?(slam dunk winner)
Q: human analogies of reserved resources (电路交换) versus on-demand allocation (分组交换)?
分组交换 对比 电路交换
Notes: slam dunk: 灌篮

## Slide 37
端系统通过接入ISP(接入 ISP)连接到互联网
  住宅、公司或大学ISP
接入ISP 必须互相连接
  以便任何两个主机能够相互之间发送分组
形成的网络的网络非常复杂
  演化由经济及国家政策所驱动
下面我们分步描述当前的互联网结构
互联网结构: 网络的网络
Notes: ISP: internet service provider

## Slide 38
Question: 给定数百万的接入 ISP, 怎样将它们连接到一起?
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
…
…
…
…
…
…
互联网结构: 网络的网络

## Slide 39
选项: 连接每一个接入 ISP 到所有其它接入 ISP?
接入
网
接入
网
…
…
…
…
…
…
…
…
直接连接每一个接入 ISP
到其它 ISP 是不可扩展的: O(N2) 个连接.
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
…
接入
网
接入
网
接入
网
接入
网
…
接入
网
接入
网
接入
网
接入
网
…
互联网结构: 网络的网络

## Slide 40
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
…
…
…
…
…
…
选项: 连接每个接入 ISP 到单一全球交换 ISP?
用户 与 提供商 ISP 具有经济协议
全球 ISP
互联网结构: 网络的网络
Notes: 单一全球交换ISP结构(single global transit ISP)

## Slide 41
ISP C
ISP B
ISP A
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
…
…
…
…
…
…
但只要有一个全球 ISP 展开了商务, 就会出现其它竞争者….
接入
网
互联网结构: 网络的网络

## Slide 42
ISP C
ISP B
ISP A
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
…
…
…
…
…
…
接入
网
但只要有一个全球 ISP 展开了商务, 就会出现其它竞争者….必须互相连接
IXP
peering link
对等连接
互联网交换点
internet exchange point
IXP
互联网结构: 网络的网络

## Slide 43
ISP C
ISP B
ISP A
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
…
…
…
…
…
…
接入
网
IXP
IXP
接入
网
接入
网
接入
网
regional 网
… 且区域网络也可能上升到连接接入网到 ISP
互联网结构: 网络的网络

## Slide 44
ISP C
ISP B
ISP A
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
接入
网
…
…
…
…
…
…
接入
网
IXP
IXP
接入
网
接入
网
接入
网
regional 网
内容提供商 网络
… 且内容提供商网络 (e.g., Google, Microsoft, Akamai) 可能运行其自有的网络, 将服务、内容送达到临近的终端用户
互联网结构: 网络的网络

## Slide 45: 互联网结构: 网络的网络
在中心: 少量相互间良好连接的大网络
  “1级” 商业 ISP (e.g., Level 3, Sprint, AT&T, NTT), 国家或国际覆盖
  内容提供商网络 (e.g., Google): 通过私有网络将其数据中心连接到互联网, 通常绕开1级或区域 ISP
IXP
IXP
IXP
1级 ISP
1级 ISP
Google
区域 ISP
区域 ISP
接入
ISP
接入
ISP
接入
ISP
接入
ISP
接入
ISP
接入
ISP
接入
ISP
接入
ISP

## Slide 46: 1级 ISP: e.g., Sprint
…
收/发 自顾客
对等操作
收/发 自骨干网
多宿(multi-home)
…
…
…
…
POP: point-of-presence
Notes: Peering: 对等操作
Transit: 不对等
上网搜索两者的差异
节点(POP): A point-of-presence is a physical location where two or more types of communication devices can establish a connection
http://www.cnpaf.net/Class/p/200510/8396.html: 在因特网上，一个节点（POP）是一个从一个位置到因特网的其它部分的进入点。一个节点必然地有一个独特的因特网（IP）位址。因特网服务提供者或在线服务供应者（比如美国在线公司）有在因特网上一个或多个节点。因特网服务提供者或在线服务供应者拥有的节点的数量有时被用来衡量这些公司的规模和成长速率。 一个节点可能实际上属于通讯公司所有，因特网服务提供者可以租借其空间来提供服务。一个节点通常包含路由器，数字/模拟信号转换器，服务器，经常还有架框继电器或非同步传输模式开关。
Multi-home: 多宿

## Slide 47: Homework
ping另外一台计算机
tracert 一个服务器
申请github账户，下载相关资源https://github.com/wireshark/wireshark
作业使用markdown格式或word(强烈建议用markdown)
用github将作业提交到课代表
作业命名格式：学号_姓名.md
每次作业在一周内提交（每次课前提交上次作业）

## Slide 48: 第一章: 目录
  1.1 什么是互联网?
  1.2 网络边缘
    端系统, 接入网, 链路
  1.3 网络核心
    分组交换, 电路交换, 网络结构
  1.4 网络时延, 丢包及吞吐量
  1.5 协议层次, 服务模型
  1.6 网络攻击: 安全
  1.7 历史
Notes: 48

## Slide 49: How do 丢包 and 时延 occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (时延)
packets queueing (时延)
free (available) buffers: arriving packets
dropped (丢包) if no free buffers

## Slide 50: Four sources of packet 时延
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing 时延
time waiting at output link for transmission
depends on congestion level of router
传播
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 51
dtrans: transmission 时延:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: 传播 时延:
d: length of physical link
s: 传播 speed (~2x108 m/sec)
dprop = d/s
Four sources of packet 时延
* Check out the Java applet for an interactive animation on trans vs. prop 时延
dtrans and dprop
very different
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
传播
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 51

## Slide 52: Caravan analogy
cars "propagate" at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to "push" entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 53: Caravan analogy (more)
suppose cars now "propagate" at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 54: Queueing 时延 (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing 时延 small
La/R -> 1: avg. queueing 时延 large
La/R > 1: more "work" arriving
than can be serviced, average 时延 infinite!
average queueing 时延
La/R ~ 0
La/R -> 1
* Check online interactive animation on queuing and 丢包

## Slide 55: "Real" 互联网 时延s and routes
what do "real" 互联网 时延 & 丢包 look like?
traceroute program: provides 时延 measurement from source to router along end-end 互联网 path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes
Notes: ICMP
Traceroute的用法为: Traceroute [options] <IP-address or domain-name> [data size]
[options]的内容有:
[-n]:显示的地址是用数字表示而不是符号
[-v]:长输出
[-p]:UDP端口设置(缺省为33434)
[-q]:设置TTL测试数目(缺省为3)
[-t]:设置测包的服务类型
[data size]:每次测试包的数据字节长度(缺省为38)

## Slide 56: "Real" 互联网 时延s, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 时延 measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org

## Slide 57: "Real" 互联网 时延s, routes
1 134.79.197.131 (134.79.197.131) [AS3671] 0.599 ms
2 rtr-core2-p2p-serv01-02.slac.stanford.edu (134.79.253.253) [AS3671] 0.502 ms
3 rtr-fwcore1-trust-p2p-core1.slac.stanford.edu (134.79.254.134) [AS3671] 0.914 ms
4 rtr-core2-p2p-fwcore2-untrust.slac.stanford.edu (134.79.254.149) [AS3671] 1.366 ms
5 rtr-border2-7k-core1.slac.stanford.edu (134.79.252.181) [AS3671] 1.304 ms
6 sunncr5-ip-c-slac.slac.stanford.edu (192.68.191.233) [AS3671] 1.692 ms
7 210.25.189.141 (210.25.189.141) [AS4538] 10.957 ms
8 *
9 210.25.187.42 (210.25.187.42) [AS4538] 163.984 ms
10 210.25.187.45 (210.25.187.45) [AS4538] 163.857 ms
11 210.25.189.69 (210.25.189.69) [AS4538] 166.290 ms
12 101.4.116.81 (101.4.116.81) [AS4538] 163.201 ms
13 101.4.114.230 (101.4.114.230) [AS4538] 183.698 ms
14 wh1.cernet.net (202.112.53.82) [AS4538] 181.983 ms
15 218.197.158.253 (218.197.158.253) [AS4538] 182.566 ms
traceroute: www.slac.stanford.edu to www.whu.edu.cn

## Slide 58: Packet 丢包
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and 丢包

## Slide 59: 吞吐量
吞吐量: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 60: 吞吐量 (more)
Rs < Rc What is average end-end 吞吐量?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end 吞吐量?
link on end-end path that constrains end-end 吞吐量
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 61: 吞吐量: 互联网 scenario
per-connection end-end 吞吐量: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 62: 第一章: 目录
  1.1 什么是互联网?
  1.2 网络边缘
    端系统, 接入网, 链路
  1.3 网络核心
    分组交换, 电路交换, 网络结构
  1.4 网络时延, 丢包及吞吐量
  1.5 协议层次, 服务模型
  1.6 网络攻击: 安全
  1.7 历史
Notes: 62

## Slide 63: 协议 "layers"
网络s are complex,
with many "pieces":
  主机
  routers
  链路 of various media
  applications
  协议s
  hardware, software
Question:
is there any hope of organizing structure of 网络?
…. or at least our discussion of 网络s?

## Slide 64: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 65: Layering of airline functionality
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing

## Slide 66: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 67: 互联网 协议 stack
application: supporting 网络 applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
网络: routing of datagrams from source to destination
  IP, routing 协议s
link: data transfer between neighboring 网络 elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits "on the wire"
application
transport
网络
link
physical

## Slide 68: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
互联网 stack "missing" these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
网络
link
physical

## Slide 69: Encapsulation
source
application
transport
网络
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
网络
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
网络
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 70: 第一章: 目录
  1.1 什么是互联网?
  1.2 网络边缘
    端系统, 接入网, 链路
  1.3 网络核心
    分组交换, 电路交换, 网络结构
  1.4 网络时延, 丢包及吞吐量
  1.5 协议层次, 服务模型
  1.6 网络攻击: 安全
  1.7 历史
Notes: 70

## Slide 71: 网络 安全
field of 网络 安全:
  how bad guys can attack 计算机网络s
  how we can defend 网络s against attacks
  how to design architectures that are immune to attacks
互联网 not originally designed with (much) 安全 in mind
  original vision: "a group of mutually trusting users attached to a transparent 网络" 
  互联网 协议 designers playing "catch-up"
  安全 considerations in all layers!

## Slide 72: Bad guys: put malware into 主机 via 互联网
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 73
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
target
1. select target
2. break into 主机 around the 网络 (see botnet)
3. send packets to target from compromised 主机
Bad guys: attack server, 网络 infrastructure

## Slide 74: Bad guys can sniff packets
packet "sniffing":
  broadcast media (shared Ethernet, wireless)
  promiscuous 网络 interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer
  https://github.com/wireshark/wireshark

## Slide 75: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload
… lots more on 安全 (throughout, Chapter 8)

## Slide 76: 第一章: 目录
  1.1 什么是互联网?
  1.2 网络边缘
    端系统, 接入网, 链路
  1.3 网络核心
    分组交换, 电路交换, 网络结构
  1.4 网络时延, 丢包及吞吐量
  1.5 协议层次, 服务模型
  1.6 网络攻击: 安全
  1.7 历史
Notes: 76

## Slide 77: 互联网 历史
1961: Kleinrock - queueing theory shows effectiveness of 分组交换
1964: Baran - 分组交换 in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (网络 Control 协议) first host-host 协议
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early 分组交换 principles

## Slide 78
1970: ALOHAnet satellite 网络 in Hawaii
1974: Cerf and Kahn - architecture for interconnecting 网络s
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s 互联网working principles:
  minimalism, autonomy - no internal changes required to interconnect 网络s
  best effort service model
  stateless routers
  decentralized control
define today’s 互联网 architecture
1972-1980: 互联网working, new and proprietary nets
互联网 历史

## Slide 79
1983: deployment of TCP/IP
1982: smtp e-mail 协议 defined
1983: DNS defined for name-to-IP-address translation
1985: ftp 协议 defined
1988: TCP congestion control
new national 网络s: CSnet, BITnet, NSFnet, Minitel
100,000 主机 connected to confederation of 网络s
1980-1990: new 协议s, a proliferation of 网络s
互联网 历史

## Slide 80
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
网络 安全 to forefront
est. 50 million host, 100 million+ users
backbone 链路 running at Gbps
1990, 2000’s: commercialization, the Web, new apps
互联网 历史

## Slide 81
2005-present
~5B devices attached to 互联网 (2016)
  smartphones and tablets
aggressive deployment of broadband 接入
increasing ubiquity of high-speed wireless 接入
emergence of online social 网络s:
  Facebook: ~ one billion users
service providers (Google, Microsoft) create their own 网络s
  bypass 互联网, providing "instantaneous" 接入 to search, video content, email, etc.
e-commerce, universities, enterprises running their services in "cloud" (e.g., Amazon EC2)
互联网 历史

## Slide 82: Introduction: summary
covered a "ton" of material!
互联网 overview
what's a 协议?
网络边缘, core, 接入 网络
  分组交换 versus circuit-switching
  互联网 structure
performance: 丢包, 时延, 吞吐量
layering, 服务模型
安全
历史
you now have:
context, overview, "feel" of 网络ing
more depth, detail to follow!

## Slide 83
第一章 Additional Slides

## Slide 84
Transport (TCP/UDP)
网络 (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received

## Slide 85: Homework
课本第一章习题任意选做3道